## Slide 1: Cool Easy
R32 Cooling & Heating
3 DC inverter

## Slide 2
Content
Product overview
SPEC
Features
Special features for Cool Easy

## Slide 3
EP24 Panel
Product overview
X outdoor unit
RG10L Remote
No | Inverter (R32) | SEER | SCOP | Operation temperature | Power supply | Remark
1 | ERP Top 9K/12K | ≥8.5 A+++ | 4.6 A++ | 16~30 ℃ | 220-240V/50/60 Hz/1Ph | European standard (EU)
2 | ERP Top 18K/24K | ≥8.5 A+++ | 4.4/4.2 A+ |  |  | 

## Slide 4
RG10 Remote Controller
RG10L
 | For fix speed type |  | For inverter type |  | 
 | RG67N | RG67B | RG67V | RG67G | RG10L
Temperature Range | 17-30 | 16-30 | 17-30 | 16-30 | 16-30
Stepless fan speed | N | N | N | Y | Y
Swing | Y | Y | Y | Y | Y
Sleep | Y | Y | Y | Y | Y
LED | Y | Y | Y | Y | Y
Turbo | Y | Y | Y | Y | Y
Follow Me | Y | Y | Y | Y | Y
Clean | Y | Y | Y | Y | Y
8° heating | Y | Y | Y | Y | Y
silence | Y | Y | Y | Y | Y
Fresh | Y | Y | Y | Y | Y
ECO | N | N | Y | Y | Y
GEAR | N | N | N | Y | Y
Wind avoid Me | N | N | N | Y | Y
Intelligent eye | N | N | N | N | Y
HUMIDITY | N | N | N | N | Y
Increased temperature in 0.5℃ | N | N | N | N | Y

## Slide 5
SPEC

## Slide 6
Features
General
 | Convenience
1 | Multi Controllers
2 | 2-way Draining
3 | Louver Position Memory
4 | Manual On & Off Button
5 | Open terminal block
 | Comfort
1 | Turbo
2 | Silence Mode
3 | Follow Me
4 | Do Not Disturb
5 | 1%~100% Grades Indoor Fan Speed
6 | Fast cooling and heating
7 | 9 Grades Outdoor Fan Speed
8 | 3D Air Flow
10 | Anti-Cold Air Function
9 | Wind Avoid Me
10 | Intelligent eye
 | Energy Saving
1 | GA compressor frequency control
2 | X-ECO Mode
3 | 8℃ Heating
4 | Sleep Mode
5 | 1W Standby
6 | Gear operation
7 | Timer
 | Health
1 | HD Dust Filter
2 | Cold-catalyst filter
3 | Active clean
4 | *Ionizer
 | Reliability
1 | Refrigerant Leakage Detect
2 | Emergency Using
3 | Low Ambient Cooling & Heating
4 | Auto Defrosting
5 | Intelligent dusting switch
Notes:* means optional.

## Slide 7
Comfort Energy saving Convenience Reliability Health
Features
Turbo
Indoor fan turns to turbo speed.
In cooling mode, the unit will keep running with turbo function..
In heating mode, the unit will keep running with turbo function.

## Slide 8
Comfort Energy saving Convenience Reliability Health
Features
Silence mode
Select SILENCE on remote controller to enter silent operation .
Press ON/OFF, Mode, Sleep button, turn on F.P. or Self clean function while operating will cancel silence function.(Model dependent)
Indoor fan will run at super breeze which keeps indoor noise as low as 20dB(A)*.
The frequency will be fixed at certain value when in silence mode.

## Slide 9
Comfort Energy saving Convenience Reliability Health
Features
Follow me
With this function, the room temperature sensor built in remote controller is activated and replaces the one in indoor unit. Then the air conditioner will regulate the room temperature based on the temperature around the remote controller, just like the air conditioner is following the user.
Pressing the “Follow me” button on remote controller to active this function. Then the remote controller will send PCB the signal every three minutes. If the PCB doesn’t receive the signal for 7 minutes or pressing “Follow me” button again, the follow me function will terminate.

## Slide 10
Comfort Energy saving Convenience Reliability Health
Features
Do Not Disturb
OFF OFF
Turn off the ring and display, which gives you a quiet and comfortable sleep.

## Slide 11
Comfort Energy saving Convenience Reliability Health
Features
1%~100%Grades Indoor Fan Speed
Via remote control, you can adjust fan speed from 1%-100%, enjoying a more comfortable cooling experience by precise wind speed control.
Au
20%
40%
60%
100%
80%

## Slide 12
Comfort Energy saving Convenience Reliability Health
Features
Fast Cooling and Heating
Like a runner sprinting to the line, this tech enables the compressor to achieve maximum frequency in split of the moment(65Hz within 6s) upon start up, providing you powerful cooling/heating once the air conditioner is on.

## Slide 13
Comfort Energy saving Convenience Reliability Health
Features
9 Grades of Outdoor fan speed
Due to the DC fan motor, outdoor fan speeds are increased from 2 grades to 9 grades, more comfortable and energy saving.

## Slide 14
Comfort Energy saving Convenience Reliability Health
Features
3D Air Flow
3D Airflow
The directional air outlet moves automatically to direct air flow to every corner of the room and keep it thoroughly cool.

## Slide 15
Comfort Energy saving Convenience Reliability Health
Features
Anti-Cold Air Function

## Slide 16
Comfort Energy saving Convenience Reliability Health
Features
Wind Avoid Me(Breeze Away)
Avoid wind blowing directly on you by using the remote
to instantly adjust the wind direction.
Wind Avoid Me

## Slide 17
Comfort Energy saving Convenience Reliability Health
Features
Intelligent eye
It could automatically switches into energy saving mode, or turns off when it detects an empty room.
Intelligent eye

## Slide 18
Comfort Energy saving Convenience Reliability Health
Features
Fmax
Fmin
● GA compressor frequency control
The frequency of traditional air conditioner has dramatic fluctuation during operation, leading to the instability of room temperature. However, Carrier air conditioners break away from this pattern with our unique GA Stepless Comfort Technology（0.6Hz for every step）. Its inverter frequency variation is so smooth that you wouldn’t notice the room temperature fluctuation at all.
Temperature Graph
GA Stepless Inverter Mode
Ordinary Inverter Mode
Fmax
Fmin
Ordinary Inverter Mode
GA Stepless Inverter Mode

## Slide 19
Comfort Energy saving Convenience Reliability Health
Features
X-ECO mode applies to inverter model, smart control on compressor frequency as low as 12HZ. As a smart running mode, it limits the highest compressor frequency and fan speed of each stage by intelligent control system.
Running at Auto fan speed
Running at ECO fan speed
First stage
Second stage
Third stage
Forth stage
Fifth stage
15 min
15 min
30 min
60 min
X-ECO

## Slide 20
Comfort Energy saving Convenience Reliability Health
Features
Electrical control logical
Press the Temperature Down button 2 times on remote controller to active this function.
Off condition:
Press On/off, Sleep, Mode, Fan and Temp. button while operating will cancel this function.
8 ℃ heating function can be memorized if the power fails.
Anti-cold wind function is inactive.
Advantage for end-user: In heating operation, the preset temperature of the air conditioner can be as lower as 8℃ (why 8℃ heating？energy saving concerned), which keeps the room temperature steady at 8℃ and prevents household things freezing when the house is unoccupied for a long time in winter.
8 ℃ heating

## Slide 21
Comfort Energy saving Convenience Reliability Health
Features
Sleep Mode
In cooling mode, the setting temperature rises 1℃(no more than 30℃) everyone hour, 2 hour later the rising stops and indoor fan is fixed at low speed.
  In heating mode, the setting temperature descends 1℃(no less than 16℃) every one hour, 2 hour later the descending stops and indoor fan is fixed at low speed, and anti-cold-air function is available.
  The unit will quit this mode and turn off after running 8 hours in sleep mode.

## Slide 22
Comfort Energy saving Convenience Reliability Health
Features
1W Standby
Intelligent on-off technology enables products automatically enter energy-saving mode when on standby mode, cut energy consumption from normal 4~5W to 0.5~1W which counts 80% of saving.

## Slide 23
Comfort Energy saving Convenience Reliability Health
Features
Carrier inverter air conditioners offer three operating
power options: 50%, 75%, and 100%.
You can choose a lower power level to conserve energy.
Gear

## Slide 24
Comfort Energy saving Convenience Reliability Health
Features
Multi Controllers
Remote Control
Central Control
Professional for commercial users
Wi-Fi Control
Operates your AC wherever you are
Wired Control
Avoid mislaying
Remote On/Off
Easy for commercial users
Note: For some units, wired controller and WI-FI control are optional, central control and remote on-off are not available.

## Slide 25
Comfort Energy saving Convenience Reliability Health
Features
2-way Draining
The refrigerant piping and drainage hose can reach either the left or right side of the indoor unit for maximum installation flexibility

## Slide 26
Comfort Energy saving Convenience Reliability Health
Features
Louver position memory
When you start the unit next time, the angle of horizontal louver will automatically move to the same position as you set last time.

## Slide 27
Comfort Energy saving Convenience Reliability Health
Features
Manual ON/OFF Button
In case the remote controller is lost, the manual mutton can be used to turn ON/OFF the unit temporary, and the structure design is more easy to access.

## Slide 28
Comfort Energy saving Convenience Reliability Health
Features
Open Terminal Block
Open Space
Broad Wiring Terminal
Narrow Space
Compact Wiring Terminal
Bigger wiring terminal &
Easier wiring connection
Time Saving
Easy installation

## Slide 29
Comfort Energy saving Convenience Reliability Health
Features
Refrigerant Leakage Detect
Indoor unit shows error code “EL0C” and stops automatically when refrigerant leakage is detected. This protects the compressor from high temperature damage due to refrigerant leakage.
This function updated base on old units, the refrigerant leakage will protect according
to T2, current , frequency, exhaust gas temperature and T1 together or more relative parameters.

## Slide 30
Comfort Energy saving Convenience Reliability Health
Features
Emergency Using
Note: when two or more sensors are abnormal, the unit will stop.
Normally, when temperature error happens, the air-conditioner will display error code and stop immediately. With this function, when temperature error happens, the air-conditioner will display error code and continue running in a proper status instead of stopping immediately, which keeps the unit in emergency working.

## Slide 31
Comfort Energy saving Convenience Reliability Health
Features
Low Ambient Cooling & Heating

## Slide 32
Comfort Energy saving Convenience Reliability Health
Features
Low Intelligent dusting switch
Apart from the bionic fan blades, the DC motor itself can constantly rotate in reverse to get rid of the sand and dust from outside, ensuring that the compressor is clean and function swell.
Rotation:
Intelligent dusting switch

## Slide 33
Comfort Energy saving Convenience Reliability Health
Features
HD Dust Filter
“Ordinary Filter” VS “HD Filter”
1 First Guard
The Dust Filter filters out dust and harmful particles from the indoor air.
2 Second Guard(optional)
The fresh filter options provide different functions to fresh the air.
Filter Type | “Ordinary “ | “HD”
Quantity of Holes per cm2 | 156 | 255
Hole Size (mm) | 1.2*1.2 | 0.54*0.54

## Slide 34
Comfort Energy saving Convenience Reliability Health
Features
Cold-catalyst Filter
Eliminate formaldehyde and other volatile
organic compounds (VOCs) as well as harmful
gases and odors.

## Slide 35
Comfort Energy saving Convenience Reliability Health
Features
Active clean
Active Clean Technology washes away dust, mold, and grease that may cause odors when it adheres to the heat exchanger by automatically freezing and then rapidly thawing the frost.
A “pi-pi” sound will be heard. The Active clean operation is used to product more condensed water to improve the cleaning effect, and the cold air will blow out.
The internal wind wheel then keeps operating to blow-dry the evaporator, thus preventing the growth of mold and keeping the inside clean.
When this function is turned on, the indoor unit display window appears “CL”, after 20 to 45 minutes, the unit will turn off automatically and cancel Active Clean function.

## Slide 36
Comfort Energy saving Convenience Reliability Health
Features
Ionizer(Optional)
Ionizer Generator can generate positive and negative ions. When positive ions meet negative ones, they will release enormous energy instantly and result in bacilli death. The redundant negative ions not only eliminates odor, dust, smoke and pollen particles in the air, but also brings more fresh.

## Slide 37
Features
Cool Easy VS 18C
Features | AE II | 18C | Features | AE II | 18C
High density filter | ● | ● | ECO | ● | ●
Cold-catalyst filter | ● | ● | Gear operation | ● | ●
Compound filter (vitamin C+Cold-catalyst+Anti-mite) | ◎ | ◎ | Sleep | ● | ●
Compound filter (Cold-catalyst+Active Carbon+silver ion) | ◎ | ◎ | 1W standby | ● | ●
UV lamp | X | ◎ | Timer | ● | ●
Self clean | X | X | GA Inverter | ● | ●
Active Clean | ● | ● | 8°C heating (Freeze Protection) | ● | ●
Optimation outdoor fan blades | ● | ● | Intelligent dusting switch | ● | ●
9 Grades of outdoor fan speed | ● | ● | Refrigerant Leakage Detect | ● | ●
1%-100% stepless Comfort | ● | ● | Louver Position Memory Function | ● | ●
Wide range voltage operation | ● | ● | Emergency Using(when temp sensor is abnormal) | ● | ●
Fast cooling/heating | ● | ● | Low Ambient Cooling | ● | ●
Crankcase Heater | ◎ | ◎ | Low Ambient Heating | ● | ●
Base Pan Heater | ◎ | ◎ | Golden Fin | ● | ●
Silence | ● | ● | Mono & Multi compatible | ● | ●
Turbo | ● | ● | I Remote (Engineering Mode) | ● | ●
Follow Me | ● | ● | On-off Control | ◎ | ◎
3D Airflow | ● | ◎ | Error Alarm port | ◎ | ◎
360℃ air supply | X | X | Centrol control | ◎ | ◎
Do not disturb | ● | ● | Wired control | ◎ | ◎
Auto-Restart | ● | ● | Wifi control | ◎ | ◎
Wind avoid me(Breeze Away) | ● | ● | AE pro installation plate | ● | X
intelligent eye | ● | X |  |  | 
● standard ◎ Optional X without

## Slide 38
Special features for Cool Easy

## Slide 39
Intelligent Eye
● standard ◎ Optional X without
When you are away for 30 minutes, automatically lowers the frequency to save energy
The unit will automatically start and resume operation if sensing human activity again.

## Slide 40
All Easy

## Slide 41
All Easy
A Short Guide:
Fast Disassembly
Of
THE CORE

## Slide 42
All Easy
A Short Guide:
Fast Disassembly
Of
THE CORE

## Slide 43
All Easy
Fast Disassembly
Of THE CORE
STEP 1
Snap Open the Front Hasps.
Detach the Bottom Panel.
Remove the Screw

## Slide 44
All Easy
Open the Electricity Box Lid
And
STEP 2
Unplug the Fan and
Vertical Louvre Motor Terminals
Fast Disassembly
Of THE CORE

## Slide 45
All Easy
Snap Open the Back Hasps
Unload the Fan and Indoor
Motor Assembly
STEP 3
Replace as You Want.
Fast Disassembly
Of THE CORE

## Slide 46: TKS!