## Slide 1
Optional Control for
QHP Hi-wall Inverter
FMCC Engineering
2022

## Slide 2
Optional Control for Hi-wall
Remote Control
Central Control/BMS Control
Professional for commercial users
WLAN Control
Operates your AC wherever you are
Wired Control
Avoid mislaying
Remote On/Off
Easy for commercial users
1. WLAN / Wired control / Central control / Dry contact can be selected only one on the same unit.
2. Remote controller can be used together with other controls.

## Slide 3
Hi-wall Control Combination QHP
Option 4-5-6 are combined in 1 Multifunction board 2209983200000A (7403034)
Note: WLAN / Wired control / Central control / Dry contact can be selected only one on the same unit.

## Slide 4
Option 1&2– Standard/WLAN Control QHP
Standard & WLAN function, No wired control function
Display PCB 1
Remote controller

## Slide 5
Option 2 - WLAN Control QHP
Working with smart phone APP
 | Display PCB 1 (Standard/WLAN function) | USB | Note
Option 1: Standard | √ |  | Remote control
Option 2.1: WLAN function without USB kit. | √ |  | If the user want to control the unit by WLAN, they have to buy the WLAN kit from Carrier
Option 2.2: WLAN Ready | √ | √ | WLAN available
USB
PN: 17310900A00681
Display PCB 1

## Slide 6
Option 2.2: WLAN Ready
WLAN kit (In the accessary bag, and put in the package)
Note:
Display PCB 1 is assembled in the unit by factory.
The WLAN kit will be put in the IDU package.
Display PCB 1
Option 2 - WLAN Control QHP

## Slide 7
Option 3 - Wired Controller 1 QHP
 | Display PCB 1 (standard) | Display PCB 2 (wired control function) | Wired controller | Note
Option 1 | √ |  |  | Remote control
Option 3.1 |  | √ |  | Need to buy wired controller separately
Option 3.2 |  | √ | √ | Wired controller available
Display PCB 2
KJR-12B without weekly timer.
KJR-120B
(PN: 17317100000004)

## Slide 8
Option 4 - Wired Controller 2 QHP
 | Display PCB 1 (standard) | Display PCB 3 (wired control function) | Transfer adapter | Wired controller | Note
Option 1 | √ |  |  |  | Remote control
Option 4.1 |  | √ | √ |  | Need to buy wired controller separately
Option 4.2 |  | √ | √ | √ | Wired controller available
Transfer adapter
(To wired controller)
Display PCB 3
KJR-120G1 with weekly timer and Error code display.
KJR-120G1/TFBG-E
(PN: 17317100A26536)

## Slide 9
Option 4 - Wired Controller 2 QHP
KJR-120G1 with weekly timer and Error code display.

## Slide 10
Option 5 – Central Control QHP
 | Display PCB 1 (standard) | Display PCB 3 (central control function) | Transfer adapter | Central Controller | Note
Option 1 | √ |  |  |  | Remote control
Option 5.1 |  | √ | √ |  | Need to buy central controller separately
Option 5.2 |  | √ | √ | √ | Central controller available
Transfer adapter
(To Central controller)
Display PCB 3
CCM30 (No Weekly Timer) CCM09 (Weekly Timer)
CCM30:
17311500A00252
CCM09: 17311500A00145

## Slide 11
Display board
Terminals board
Adaptor board
For central control, connect to XYE (Red Mark terminals).
Option 5 – Central Control QHP

## Slide 12
Option 6 – Dry Contactor Control (On/Off) QHP
 | Display PCB 1 (standard) | Display PCB 3 (Dry contact function) | Transfer adapter | Note
Option 1 | √ |  |  | Remote control
Option 6 |  | √ | √ | On/Off switch is provided in field.
Transfer adapter
(To On/Off switch)
Display PCB 3
Transfer Adapter connection wire (3-core)
PCB connection wire (4-core)
PCB
connection wire (2-core)

## Slide 13
Option 6 – Dry Contactor Control (On/Off) QHP
Display board
Terminals board
Adaptor board
There are reserved ports for connecting a remote switch to control the unit to run or stop.
NOTE: If there is no remote switch connected, these 2 ports should be short connected.
Short connecting wire (Standard)
If the short wire is missing, there will be “CP” error code.
Remote ON/OFF switch

## Slide 14
Part 2
Optional Control for new QHP Hi-wall

## Slide 15
Hi-wall Control Combination new QHP-01
Note: WLAN / Wired control / Central control / Dry contact can be selected only one on the same unit.
Display PCB, transfer adapter and 12 V cable will come as 1 multi function kit PCB (22099832000008)
7403035

## Slide 16
Thank you!